## Slide 1
Dynamic Analysis ​of Suspension System​
of An Electric Bus​

## Slide 2
Dynamic analysis ensures optimal ride comfort, stability, and safety
1
Suspension systems are vital for vehicle safety, comfort, and performance, especially with heavy battery packs and unique chassis designs.
2
It helps evaluate ride quality and design of springs, dampers, and actuators.
3
INTRODUCTION
Suspension isolates the bus body from road irregularities and transmits steering and braking loads.
4

## Slide 3
PHYSICAL MODEL DEVELOPMENT​

## Slide 4
SYSTEM COMPONENETS
Sprung Mass Components:​
  Vehicle Body: Chassis frame, battery pack, passenger cabin​
  Powertrain: Electric motor, transmission, power electronics​
  Payload: Passengers, driver, interior equipment​
  Total Sprung Mass (Ms): 9,000 – 13,000 kg (for 12m electric bus)​
Unsprung Mass Components:​
  Axle assembly, wheel hub, brake assembly​
  Wheel & Tire (rim + tire)​
  Suspension mounts (lower control arm, knuckle)​
  Total Unsprung Mass (Mu): 250 – 400 kg per wheel​
Primary Spring : Air suspension bellows or coil spring​
  Stiffness: 300,000 – 665,000 N/m​
  Natural frequency: 1 – 2 Hz​
Damper (Shock Absorber) : Hydraulic or magnetorheological​
  Damping coefficient: 12,000 – 50,000 Ns/m​
  Damping ratio: 0.2 – 0.4
​
Tire Characteristics​
  Tire stiffness Kt = 500,000 – 1,000,000 N/m​
  Tire damping Ct ≈ 10–15% of suspension damping​
  Tire sizes 245/75 R16 to 275/70 R22.5​
SUSPENSION ELEMENTS

## Slide 5
SYSTEM BEHAVIOUR :
Suspension acts as multi-stage vibration isolation:
STAGE | FUNCTION
Tire | First isolation from road irregularities
Suspension | Main isolation between sprung & unsprung masses
Load path | Road → Tire → Unsprung mass → Suspension → Sprung mass

## Slide 6
Component | Symbol and units | Meaning
Sprung mass | Ms (kg) | 1/4 vehicle body mass
Unsprung mass | Mu (kg) | Wheel + hub assembly
Suspension spring | Ks (N/m) | Suspension stiffness
Suspension Damper | Cs (Ns/m) | Suspension damping
Tire spring | Kt (N/m) | Tire stiffness
Tire Damping | Ct (Ns/m) | Tire damping
Simplified Model Development
Represents one corner of vehicle

## Slide 7
Motion Variables
  Displacements: Zs(t), Zu(t), Zr(t)​
  Velocities : Żs(t), Żu(t)​
  Accelerations: Z̈s(t), Zu(t)
Where:​
  Zs = sprung mass displacement​
  Zu = unsprung mass displacement​
  Zr = road input profile

## Slide 8
Natural Frequencies and Damping Ratios
  For passenger comfort, fs should be in the range of 1.0 - 2.0 Hz.
Unsprung Mass Natural Frequency:
  Typically, fu is in the range of 10 - 15 Hz.
Damping Ratio:
  Optimal damping ratio for passenger vehicles: ζ = 0.2 - 0.4
Sprung Mass Natural Frequency:

## Slide 9
Transfer Functions
Transmissibility:

## Slide 10
parameter​ | value
Ms​ | 2500 – 3250 kg​
Mu​ | 300 kg​
Ks​ | 250,000 - 400,000 N/m​
Cs​ | 20,000 Ns/m​
Kt​ | 800,000 N/m​
Ct​ | 2,000 Ns/m​
Mathematical model implementation
System parameter values

## Slide 11
Road excitation :​
  Bump : sinusoidal, 0.05m amplitude, wavelength 5m
  Random: ISO 8608 Class B
  Random: ISO 8608 Class B
Reference :https://www.extrica.com/article/20271

## Slide 12
Performance Metrics

## Slide 13
MATLAB CODE​
Link to matlab code: ​
https://drive.google.com/file/d/1tLqO5NefZr00L9HyUYItyZSDnxJa9833/view?usp=drivesdk

## Slide 15
Plots
4

## Slide 16
Random Road Surface plot

## Slide 17
Results
4
Conclusion
  The 2-DOF quarter-bus model provides valuable insight into ride dynamics for electric buses.​
  Suspension stiffness/damping tuning can significantly impact comfort and safety​
  Increased unsprung mass for in-wheel motors may require stiffer/active suspensions.​
  Future work: Model pitch/roll (half/full-bus), integrate field data, simulate active suspension strategies.​
References
  Sekulić, D., et al. (2014). Effects of Suspension Stiffness and Damping on Bus Ride Quality. International Journal of Vehicle Systems Modelling and Testing, 9(3), 209-225.
  Long, X., et al. (2018). Dynamic Modeling and Ride Comfort Analysis of a Full Vehicle Bus Model. Journals of Vehicle Engineering and Technology, 2018(3), 45-59.​
  https://journals.sagepub.com/doi/10.1155/2014/269721

## Slide 18
THANK YOU
Presented by :​
B . DEEPIKA (230103026)​
BHASKAR SONOWAL (230103027)​
BIBUNGSHA BORO (230103028)​
C . LIKITHA REDDY (230103029)​